## Slide 1: Iodine-131 Wholebody Dosimetry
Principal Clinical Scientist
Paediatric Nuclear Medicine & SMaRT Kids
Royal Hospital for Children, Glasgow
Dr Hugh J Wallace
IDUG Workshop – BNMS 2026

## Slide 2: The Plan
Theory
Why Wholebody Dose?
Making Measurements
Getting to Dose
Practical
Workshop Cases

## Slide 3: Why Wholebody Dose?
Correlates with blood dose
  Which correlates with bone marrow dose
  Which correlates with haemotoxicity
  Which is the dose limiting acute toxicity for Iodine-131
Allows standardisation based on toxicity
  No haemotoxicity up to 2Gy
  Stem cell transplant required at 4Gy
 Reliable patient management

## Slide 4: Why Wholebody Dose?
Straightforward to measure
  You’re probably already gathering it for discharge
~Straightforward to calculate
  Single excretion curve
  Single weight-based S-Factor

## Slide 5: Why Wholebody Dose?
Fixed-activity and weight-based are not good enough
Fixed 3700MBq:
   0.13 - 0.39 Gy
  Factor of x3
1.06x10-4 Gy/MBq
0.35x10-4 Gy/MBq

## Slide 6
Correlation of administered activity of 131I-mIBG/kg and wholebody radiation dose
Matthay et al. 2001 J Nucl Med https://pubmed.ncbi.nlm.nih.gov/11696644/

## Slide 7
Matthay et al. 2001 J Nucl Med https://pubmed.ncbi.nlm.nih.gov/11696644/
Factor of
x5
Upper ~ 1.0 x Activity/kg
Lower ~ 0.2 x Activity/kg
Correlation of administered activity of 131I-mIBG/kg and wholebody radiation dose

## Slide 8: Making Measurements
The Goal
Total activity vs time over multiple days
Requires
Equipment
Data recorded
Methodology
200
150
100
50
0
Time
4000
3000
2000
1000
0
Activity (MBq)
Measurement (units)
Time

## Slide 9: Making Measurements
Equipment
Essential:
  Linear response
  Suitable range
  Backup available
Nice to have:
  Fixed installation (e.g. ceiling mounted)
  Energy compensated
  Calibrated

## Slide 10: Making Measurements
Data Recorded
Administered Activity + Date + Time
Patient weight
Measurement + Date + Time
Patient status (e.g. post void)
Geometry (e.g. distance, bed height)

## Slide 11: Making Measurements
Data Recorded
Administered Activity + Date + Time
Patient weight
Measurement + Date + Time
Patient status (e.g. post void)
Geometry (e.g. distance, bed height)
 Recording reinforces good practice

## Slide 12: Making Measurements
Methodology
First measurement () before excretion
  or you’ll be measuring the urine too
  Perhaps the most essential thing to get right
Later measurements after excretion
  or you’ll only be measuring physical decay

## Slide 13: Making Measurements
Methodology
All measurements consistent geometry
  or you may as well make up the numbers

## Slide 14: Making Measurements
What about frequency?
Frequency | Schedule | Example Timings (h) | Potential Contributing Factors
Ideal | Multiple optimised time points per day | 0, 2, 4, 6, 8, 10 20, 22, 24, 28, 32 44, 48, 52, 60 | Well staffed centre Strong interest in dosimetry Nurses/C&Cs able to measure Compliant patient
Good / Adequate | 2 per day | 0, 8 22, 32 48, 56 | Busy centre / less staffing Nurses/C&Cs unable to measure Less compliant patient
Minimum | 1 per day | 0 24 48 | Very busy centre / minimum staffing Nurses/C&Cs unable to measure Poorly compliant patient

## Slide 15: Making Measurements
Examples
The Christie
Daily/Twice by staff
Ceiling monitor, bed lowest position
Anterior/Posterior for geomean
Addenbrooks
Hourly by patient
1m readings, floor markings
Anterior only

## Slide 16: Getting to Dose
Recall the MIRD equation:
For us,
target () = source () = wholebody ():
This leaves us with only(?) two steps:
  Use our time-activity data to calculate
  Multiply by an appropriate S-Factor

## Slide 17: Getting to Dose
Cumulated Activity
is the area under the curve  we need to integrate
A few options:
Mono-exponential fit
Bi-exponential fit
Trapezoidal (numerical) integration

## Slide 18: Getting to Dose
Mono-Exponential Fit
A simple equation:
A simple integral:
Where is the effective half-life:

## Slide 19: Getting to Dose
Bi-Exponential Fit
Equation:
And since :
Integration is the same but messier:

## Slide 20: Getting to Dose
Trapezoidal Integration
Sums trapezoidal sections:
e.g. 1500MBq @ 24h  500MBq @ 48h:
4000
3000
2000
1000
0
Activity (MBq)
Time

## Slide 21: Getting to Dose
Trapezoidal Integration
Sums trapezoidal sections:
But what about the “tail”?
  Could use physical half-life?
  Could assume mono-exponential?
4000
3000
2000
1000
0
Activity (MBq)
Time

## Slide 22: Getting to Dose
MIRD S-Factor
Modelled for newborn, 1y, 5y and adult (Snyder 1975)
Can fit these to model S-Factor vs weight (Buckley 2009):
Where is patient weight, measured in kg

## Slide 23: Getting to Dose
Some Complications
Chart: Early Redistribution
| 0 | 2.4699999999999998 | 5 | 7.17 | 17.5 | 19.52 | 23.59 | 26.52 | 31.34 | 41.17 | 43.27000000000001 | 47.70000000000001 | 50.220000000000006 | 55.5 | 67.02
Raw A -T Data | 3816.18 | 3782.52 | 3649.66 | 3405.36 | 2602.76 | 2402.14 | 2153.02 | 1862.39 | 1686.13 | 1095.05 | 1034.05 | 849.86 | 803.34 | 695.46 | 504.24
Mono-exponential fit curve | 3816.18 | 3566.7496 | 3328.1531 | 3136.2639 | 2363.9561 | 2236.8223 | 2001.0552 | 1846.8674 | 1618.637 | 1236.8551 | 1167.7775 | 1034.4489 | 965.514 | 835.613 | 609.6614
Bi-exponential fit curve | 3816.18 | 3566.7497 | 3328.1531 | 3136.264 | 2363.9562 | 2236.8224 | 2001.0554 | 1846.8675 | 1618.6371 | 1236.8552 | 1167.7776 | 1034.449 | 965.5141 | 835.6131 | 609.6615
Chart: Measurement fluctuations
| 0 | 0.85000000000000009 | 2.3499999999999996 | 5.0100000000000007 | 6.6800000000000006 | 19.03 | 23.53 | 26.3 | 31.18 | 40.35 | 45.41 | 50.600000000000009 | 55.18 | 64.679999999999993 | 66.010000000000005
Raw A -T Data | 5728.01 | 5370.46 | 4595.01 | 3782.77 | 3355.84 | 2393.63 | 1643.91 | 1284.21 | 945.62 | 708.83 | 522.22 | 361.68 | 279.88 | 188.77 | 172.98
Bi-exponential fit curve | 5728.01 | 4941.5289 | 3981.0671 | 3055.4866 | 2737.2301 | 1849.0166 | 1663.7221 | 1560.1219 | 1393.5462 | 1127.4294 | 1003.0322 | 889.6856 | 800.3488 | 642.6183 | 623.1713

## Slide 24: With Thanks
Jill Tipping (The Christie)
Sarah Heard (Addenbrooke’s Hospital)
Jon Gear (The Royal Marsden Hospital)
Bruno Rojas (The Royal Marsden Hospital)
Michael Gornall (Kings College Hospital)
Matt Aldridge (Kings College Hospital)
Colin Brown (Gartnavel General Hospital, Glasgow)

## Slide 25: Key References
EANM Dosimetry Committee series on standard operational procedures for internal dosimetry for 131I mIBG treatment of neuroendocrine tumours, Gear et al, 2020
EANM Dosimetry Committee guidelines for bone marrow and whole-body dosimetry, Hindorf et al, 2010
Dosimetry and thyroid cancer, Lassman et al, 2010
EANM Dosimetry Committee series on standard operational procedures for pre-therapeutic dosimetry, Lassman et al, 2008
Correlation of tumor and whole-body dosimetry with tumor response and toxicity in refractory neuroblastoma treated with (131)I-MIBG, Matthay et al 2001

## Slide 26: Workshop
Case 1a. “Good data” Many points
Case 1b. “Good data” 24hr data
Case 2a. “Good data” Many points
Case 2b. “Good data” 24hr data
Case 3a. Wobbly data
Case 3b. Wobbly data, excluded points
Case 3c. Wobbly data 24hr only
Case 4a. Redistribution
Case 4b. Redistribution peak adjust
Case 5. I-123 to I -131 dose calculation.